STPH 6.0 Bidding Specifications

1.0 INTENT

It is the intent of this specification to provide for the purchase of one (1) new and unused Truck Mounted Asphalt Heater to be used for the purpose of maintaining proper working temperature of hot mix asphalt.

The following specification is based upon a Stepp Mfg STPH 6.0 Truck Mounted Premix Heater. The Public Works Department has evaluated different styles of asphalt hotbox equipment and has determined that this product is best suited for the DPW needs in terms of quality and features.  This specification shall not be interpreted as restrictive but rather as a measure of quality and performance against which all other Truck Mounted Premix Heaters will be compared.

In comparing proposals, comparison will not be confined to price only.  The successful bidder will be one whose product is judged as best serving the interests of the DPW when price, product, quality and delivery are considered. The DPW also reserves the right to reject any or all bids or any part thereof, and to waive any minor technicalities. A contract will be awarded to the bidder submitting the lowest responsible bid meeting the requirements.

2.0 EQUIVALENT PRODUCT

Bids will be accepted for consideration on any make or model that is equal or superior to the hot box specified.  Decisions of equivalency will be at the sole interpretation of the DPW.  A blanket statement that equipment proposed will meet all requirements will not be sufficient to establish equivalence. An original manufacture’s brochure of the proposed product is to be submitted with proposal.

3.0 INTERPRETATIONS

In order to be fair to all bidders, no oral interpretations will be given to any bidder, as to the meaning of the specification documents or any part thereof.  Every request for such a consideration shall be made in writing.  Based on such inquiry, the DPW may chose to issue an Addendum in accordance with local state laws.

4.0 GENERAL

The specification herein states the minimum requirements of the DPW. All bids must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The DPW will consider as irregular or non-responsive any and all bids that are not prepared and submitted in accordance with the bid document and specification, or any bid lacking sufficient technical literature to enable the DPW to make a reasonable determination of compliance to the specification.  It shall be the bidder’s responsibility to carefully examine each item of the specification. Failure to offer a completed bid or failure to respond to each section of the technical specification (COMPLY: YES NO) will cause the proposal to be rejected without review as non responsive. All variances, exceptions and/or deviations shall be fully described in the appropriate section. Deceit in responding to the specification will be cause for rejection.

5.0 SPECIFICATIONS

COMPLY

YES	NO

HOPPER:

Hopper shall have a capacity of 6 cubic yard.				____	____

The unit mounted on the chassis shall have an overall dimension

of 185” long 115” high and 96” wide. The hopper with shoveling

pan shall have an overall dimension of 185” long 69” tall and 96”

wide. The empty weight of the unit to be approximately 8500

pounds. The inner tank shall have a slope of 32º.				____	____

Triple wall construction, inner hopper to be constructed of 10 gauge

material. 									____	____

Oil jacketed chamber to be constructed of 10 gauge material insulated

with 2" of 1½# density hi-temperature fiberglass insulation. The oil tank

Shall have 230 gallons of heat transfer oil minimum.			____	____

The unit shall have 2 lateral heat baffles designed into the hopper to

help evenly distribute heat into the center of material. The baffles shall

have heat transfer oil circulated through them. Insulation covers to be 16

Gauge.										____	____

Hopper shall be covered with two (2) 16 gauge hydraulically operated

doors.  										____	____

The doors shall open a full 270º to allow full hopper access for filling

while having the lowest overall height. Doors shall open with hydraulic

driven gear boxes. Door shall be double walled and insulated with 2”of

spray foam polyurethane R9 per inch insulation.				____	____

Door operation will be controlled from rear curb side of unit and a

warning buzzer will sound during door operations. 				____	____

Material will be delivered to the rear of the unit by means of an auger.

The material is discharged onto a shovel platform, swing chute(optional)

or directly onto the repair site on the roadway. 				____	____

The shoveling platform shall fold up to allow material to be dispensed

on the road way. The platform will have a lock to lock the platform in

up position.									____	____

The auger will be 6" diameter with hardened flighting and hardened 	YES	NO

auger trough. Auger flighting shall be 3/8”thick by 6” diameter

AR 400(abrasion resistant) steel.						____	____

Auger will be powered by a 2 speed 32 cubic inch hydraulic motor with

forward and reverse capability. 						____	____

To be controlled from rear street side of unit.  Auger shaft will be coupled

to the hydraulic motor by a flexible coupling to allow for movement. Support

bearing to be 1½” with permanently lubricated, sealed ball bearings with

hi-temperature seals.			  					____	____

Hopper shall have a thermostat in the hopper to monitor the temperature

of the material and to monitor the heat transfer oil temperature.		____	____

Temperature gauges to be digital and be intergraded into the thermostat

control and shall monitor product temperature and heat transfer oil

temperature and optional tack tank.						____	____

Hopper shall be mounted to the truck chassis with a spring loaded slip

saddle mount.									____	____

Constructed with side mounted storage compartments for tool storage.

Tool storage area to also accommodate  optional items such as tack tank.	____	____

HEATING SYSTEM FOR HOPPER:

Unit will be equipped with a 12 Volt Beckett Diesel Burner with up to

490,000 BTU output, firing into a 12” heating chamber transitioning

down to a 6” x .188 fire tube.							____	____

Heat transfer oil shall surround the sides and bottom of hopper and

circulate thru heat risers for even material heating.  The fire tube will

run from along the bottom of the oil jacket and return to a vertical

stack exhausting into the top of the hopper to reduce bridging.		____	____

Equipped with automatic temperature control, spark ignition with flame

sensing for automatic shut down of main diesel burners in case of flame

out. To be equipped with all necessary fittings, hoses and valves. 		____	____

The flue will be equipped with one (1) replaceable 309 stainless steel

diffuser to prevent hot spots in heating chamber. 				____	____

The diesel burner fuel is supplied from a 20 gallon fuel tank mounted

on the front of the hook frame.						____	____

A hydraulic operated heat transfer oil pump shall be included to

circulate the hot oil evenly around the hopper for even heating.		____	____

YES	NO

HYDRAULIC SYSTEM:

The hydraulic pump shall be mounted directly to PTO of truck. 		____	____

Pump shall be load sensing, variable displacement, piston pump with

an operating pressure of 2000 PSI (power take off to be included). 		____	____

The hydraulic pump shall be an axial piston pressure and flow compensated

load-sensing type. The pump shall have a displacement of 5.61 cubic

inches per revolution at maximum stroke which will deliver 23.7 gpm @ 1000

engine rpm.  The pump shall have a minimum 2” inch suction line and ½”

control drain line plumbed directly back to the reservoir.  The pumps

compensator shall have rear facing adjustments.  The pump shall be rated

for 5800 PSI maximum and 4800 PSI continuous. The operating pressure

of the unit shall be 2000PSI. The pump shall have a Din type-mounting

flange and a Din 5462 8-tooth shaft.  The pump shall be FORCE America

TXV92 or prior approved equal. An OMFB series constant mesh PTO

that is mounted to the transmission shall drive the pump.  			____	____

Hopper shall have hydraulic controls for discharge auger, hot oil

circulating pump, and top cover. 						____	____

Valve to be a Force America Add-A-Fold. The valve sections shall be rated

at 20GPM. The hydraulic valve shall be of modular manifold design.  Each

hydraulic function requires an individual manifold stacked together to form

the manifold base.  The manifold base shall consist of an inlet section with

SAE #16 inlet porting, SAE #20 outlet  porting, and SAE #4 load sense

porting.  There shall be a main system relief in the inlet section to protect

the system from high pressure in case the pump compensators fail.  Each

hydraulic valve segment shall be individually mounted to the manifold base

assembly and be serviceable without removing any hydraulic hoses or any

other hydraulic valve segments.  Each hydraulic valve segment shall have

individual pressure compensation to achieve independent simultaneous

operations.  All segments shall have heavy-duty continuous duty coils

and connections shall be with Din connectors.  All coils shall operate

at 12 VDC and require a maximum of 1400 mille-amps.  Each segment

shall be equipped with a manual overrides.  					____	____

All hydraulic lines to be run in steel tubing with face seal fittings.		____	____

A 30 gallon oil reservoir and valve enclosure combination shall be

included. A ventilated fill cap, filter, hydraulic cooler and sight/

temperature gauge shall be included.						____	____

OPTIONAL TACK TANK:

Unit shall have an 80 gallon tack tank integrated into the hopper.		____	____

Tack system to be driven hydraulically and have a heat transfer oil

heating system that is thermostat ally controlled. 				____	____

The thermostat shall have a digital readout that displays both set

and actual product temperature and be adjustable from 0-550ºF.		____	____

Shall include a hand wand which shall be 48”x ½” and equipped with a

Vee-jet nozzle with fan spray. 						____	____

Wand shall have a twist style shut off valve due to spring or dead man

valves not operating with sticky asphalt material. 				____	____

Sprayer hose to be 15’x ½” and system to have solvent flushing

capabilities.									____	____

Spray system to operate from rear curb side of the machine with a

re-circulating port to allow product to circulate back to tank through

the wand.									____	____

Asphalt pump shall be a positive displacement 10 GPM self-priming

pump. 	The pump shall be a Viking FH32 and be driven by a 1.5 CID

hydraulic motor with forward and reversing capabilities.			____	____

The pumping system shall have a WPC (wand pressure control valve)

In place of relief valve. Relief valves do not function properly with

asphalt materials due to the sticky nature of the material. The WPC

valve adjusts wand pressure and relieves pressure when wand is off.	____	____

LIGHTS:

Lights will be seal beam style. Rubber grommet mount. All lighting

shall meet state and federal regulations of the FMVSS. 			____	____

PAINT:

To be primed with primer and painted highway black unless otherwise

specified. Paint to be a 2 part poly urethane paint minimum 6 mils thick.	____	____

WARRANTY:

One (1) year on workmanship and manufactured equipment.  		____	____

OPTIONAL FEATURES:							YES	NO

HOOK MOUNTED:

Unit shall  be equipped with a hook truck hitch to allow the addition of

other types of equipment.							____	____

Hook Mounted Hydraulic System

Hopper shall utilize hydraulic pump from the hook system on the truck.

A manifold shall be installed in between the hydraulic pump and the

trucks valve to operate the hook system. The manifold will have 3

hydraulic quick connectors for the pressure line, return line and the load

sense line. This will allow both hydraulic valves, hopper and hook, to

operate simultaneously.				  			____	____

Pump shall be load sensing, variable displacement, piston pump with

an operating pressure of 2700 PSI (power take off to be included). 		____	____

Hopper shall have hydraulic controls for discharge auger, hot oil

circulating pump, and top cover. 						____	____

Valve to be a Force America Add-A-Fold. The valve sections shall be rated

at 20GPM. The hydraulic valve shall be of modular manifold design.  Each

hydraulic function requires an individual manifold stacked together to form

the manifold base.  The manifold base shall consist of an inlet section with

SAE #16 inlet porting, SAE #20 outlet  porting, and SAE #4 load sense

porting.  There shall be a main system relief in the inlet section to protect

the system from high pressure in case the pump compensators fail.  Each

hydraulic valve segment shall be individually mounted to the manifold base

assembly and be serviceable without removing any hydraulic hoses or any

other hydraulic valve segments.  Each hydraulic valve segment shall have

individual pressure compensation to achieve independent simultaneous

operations.  All segments shall have heavy-duty continuous duty coils

and connections shall be with Din connectors.  All coils shall operate

at 12 VDC and require a maximum of 1400 mille-amps.  Each segment

shall be equipped with a manual overrides.  					____	____

All hydraulic lines to be run in steel tubing with face seal fittings.		____	____

HOPPER ACCESS WALKWAYS

Shall have front and rear built-in steps with a fold down hopper access

platform with raised grip tread and non-skid surface.			____	____

LP HAND TOURCH

Unit to be equipped with a 125,000 BTU Hand Torch with shutoff valve

and 15’ of LP hose and 20# cylinder and bottle rack.			____	____

ASPHALT SWING CHUTE:

Folding asphalt chute in place of shoveling pan.  Swings right and

left and has locking positions. 						____	____

HYDRAULIC POWER BEYOND:

Hydraulic power beyond to power hydraulic jack hammer or

hydraulic tamper. 								____	____

STANLEY BR67 BREAKER:

Stanley BR67 hydraulic 70# class jack hammer.				____	____

DUAL HYDRAULIC HOSE REEL:

Dual Hydraulic hose reel to be used with hydraulic jack hammer		____	____

SHOVEL CLEANING COMPARTMENT:

Shall have a Shovel Cleaning Compartment constructed of 12 gauge

material with splash guard compartments, drain plug, and rain tight

cover. Shall hold (4) four shovels. 						____	____

COMPACTOR PLATE CARRIER:

Compactor Plate Carrier with hydraulic raise and lower for operator

convenience and shall have a spring lock and fold up out of the way when

not in use.									____	____

SPOILS BIN:

Shall include a Spoils Bin constructed of 10 gauge steel with trap door

in bottom. Capacity of 6 cubic feet located on right side of unit in front

of rear axle.									____	____

WASH DOWN SYSTEM:

Wash down System with a 12V.D.C. pump with application hose and

wands for cleaning tools and hopper. Shall be pumped from truck fuel

tank and interfaced with burner shutoffs when the wash down is in

operation			.						____	____

AIR BLAST SYSTEM:

Shall be equipped with air that is supplied to an auxiliary tank by the

truck air compressor to enable operator to provide a short blast of air to

clean out small potholes. A safety valve incorporated into the air system

to prevent loss of air to the air brake system. Shall include 25’ of 3/8”

air hose with blow stick handle. 						____	____

STAINLESS STEEL TOOL HOLDERS:

(2) Stainless Steel Tool Holders-spring loaded clamps mounted

vertically for holding rakes, shovels and lutes.				____	____

LED LIGHTING;

Unit shall include LED lighting,				. 		____	____

RECPROCATING AIR COMPRESSOR:

Reciprocating air compressor to be powered from the truck hydraulic system.

Truck engine will have to run above idle speed to operate. Air compressor

shall be used to clean debris from potholes. Shall have 25 cfm rating.	____	____

ROTARY SCREW COMPRESSOR:

An optional rotary screw air compressor shall be powered from under hood,

serpentine belt drive off of truck engine. Shall have a 100 CFM output

capable of handling air tools such as a jackhammer. Compressor shall

have air tank  plumbed to rear of unit with glad hand connectors. Hose

available as optional.					 			____	____

OVERNIGHT ELECTRIC HEATER:

Allows for a faster start-up and helps to maintain heat. The hopper shall

have 2-3000 watt, 230 V.A.C, connected to the same thermostat as the

diesel heater and wired to a 10'-8 gauge extension cord for overnight

heating. The tack tank, when included, shall have 1-1500 watt heater

wired to the same thermostat as the tack tank.				____	____

ARROWSTICK:

Optional arrow stick for increased operator safety. Mounted on the top

rear of hopper with controller in the operators control panel.		____	____

STROBE LIGHTS:

Optional Flashing Beacon or flush mounted LED strobes.			____	____

DOT LIGHTING SYSTEM:

Shall be a Whelen Super LED lighting system to include Stop, Tail ,

Turn, Rear Amber  Strobes, and 2 Mirror Mounted  Strobes. 		____	____

HOOK MOUNTED;

Unit can be equipped with a hook truck hitch to allow the addition of

other types of equipment.							____	____

HOSE REELS:

Spring rewind hose reels for tack hose, lp hand torch hose and wash

down hose. 									____	____

ASPHALT ANTI-BRIDGING BREAKER:

Shall consist of a 2” schedual 40 shaft with oposing arms mounted in

the middle of the unit and operate hydraulically with a 1 ½” hydraulic

cylinder. The shaft shall have 2 sealed bearings. The breaker shall

agitate right and left to break up any material that may hang up.		____	____

Exceptions & Deviations

Bidder shall fully describe every variance exception and/or deviation.  List the item number here and fully explain any items in non-compliance with specification.   Additional sheets may be used if required.

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________