Stepp Manufacturing Co Inc

Model Stph-5.0 Pothole Patcher Truck Requirements

35,000# GVWR

12,000# Front Axle

23,000# Rear Axle

120” Cab to Axle Length

195” Wheelbase (may vary with different truck mfg)

Transmission

Automatic transmission with PTO Flange

Manual Transmission requires extended front bumper and capabilities for crankshaft driven PTO.

Stepp to supply PTO, pump, tank, and all motors and plumbing to operate hydraulic driven pumping system.

Exhaust System

We prefer a vertical exhaust system if possible. If exhaust system is overly large we may need to extend the cab to axle to accommodate the larger stacks and mufflers. Please contact us if you have any questions.

Clear Frame Space

Spoils Bin. The spoils bin will be mounted on the curb side of the unit requiring 43” of free space. If interference with truck accessories is an issues we can do custom mounts for an additional fee.

Hydraulic Tank and Valve Enclosure. The Hydraulic tank and valve enclosure shall be mounted on the street side of the unit requiring 53” of clear frame space.

If you have any questions please feel free to contact us at 651-674-4491.

Updated and verified 10/28/2015