SPH-2.0 Pre-Mix Heater

Bidding Specifications

1.0 INTENT

It is the intent of this specification to provide for the purchase of one (1) new and unused portable asphalt storing, heating and dispensing box to be used for the purpose of maintaining proper working temperature of hot mix asphalt.

The following specification is based upon a Stepp Mfg Portable SPH 2.0 Hot Box Premix Heater. The Public Works Department has evaluated different styles of asphalt hotbox equipment and has determined that this product is best suited for the DPW needs in terms of quality and features.  This specification shall not be interpreted as restrictive but rather as a measure of quality and performance against which all other Portable Hot Box Premix Heaters will be compared.

In comparing proposals, comparison will not be confined to price only.  The successful bidder will be one whose product is judged as best serving the interests of the DPW when price, product, quality and delivery are considered. The DPW also reserves the right to reject any or all bids or any part thereof, and to waive any minor technicalities. A contract will be awarded to the bidder submitting the lowest responsible bid meeting the requirements.

2.0 EQUIVALENT PRODUCT

Bids will be accepted for consideration on any make or model that is equal or superior to the hot box specified.  Decisions of equivalency will be at the sole interpretation of the DPW.  A blanket statement that equipment proposed will meet all requirements will not be sufficient to establish equivalence. An original manufacture’s brochure of the proposed product is to be submitted with proposal.

3.0 INTERPRETATIONS

In order to be fair to all bidders, no oral interpretations will be given to any bidder, as to the meaning of the specification documents or any part thereof.  Every request for such a consideration shall be made in writing.  Based on such inquiry, the DPW may chose to issue an Addendum in accordance with local state laws.

4.0 GENERAL

The specification herein states the minimum requirements of the DPW. All bids must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The DPW will consider as irregular or non-responsive any and all bids that are not prepared and submitted in accordance with the bid document and specification, or any bid lacking sufficient technical literature to enable the DPW to make a reasonable determination of compliance to the specification.  It shall be the bidder’s responsibility to carefully examine each item of the specification. Failure to offer a completed bid or failure to respond to each section of the technical specification (COMPLY: YES NO) will cause the proposal to be rejected without review as non responsive. All variances, exceptions and/or deviations shall be fully described in the appropriate section. Deceit in responding to the specification will be cause for rejection.

5.0 SPECIFICATIONS

COMPLY

HOPPER:									YES	NO

Unit shall be portable, trailer mounted 					____	____

Frame shall be constructed of welded steel					____	____

Frame shall meet or exceed all DOT safety regulations			____	____

Trailer to meet NATM Certifications and include proper tire labeling.	____	____

Length shall not be less than 208” inches. Anything shorter than this

will not tow well due to weight and balance issues.				____	____

Width shall not exceed 90"							____	____

Height shall not exceed 76”							____	____

Weight shall be approximately 3,750. lbs. (including trailer)		____	____

Minimum storage capacity shall be 2.0cy					____	____

Walls shall be minimum triple wall construction				____	____

Wall insulation shall be minimum 2” of 1½# density hi-temperature

fiberglass.									____	____

Outer shell construction shall be a minimum 16 gauge thick steel		____	____

Heat Jacket walls shall be minimum 12 gauge				____	____

Heat jacket diffuser shall be constructed of 309 stainless steel and have

an adjustable heat baffle.							____	____

Frame shall be constructed of high strength rectangular steel tubing 	____	____

Frame shall be reinforced at all stress points					____	____

Shall have (2) vertical tubing legs constructed of 2”x6”x3/16” and

(2) rear legs that are formed ¼” steel welded to hopper.			____	____

Frame tubing shall have a minimum thickness 2”x 6”x 3/16” 		____	____

Hopper shall be bolted to frame in (4) places.				____	____

6.0 Loading Doors								YES	NO

Top loading doors shall be covered with a minimum of 16 gauge steel.	____	____

Top load doors shall utilize gas assist shocks with steel lock downs and

latches on handles.								____	____

Door handles shall be ½” steel with round rubber grips and shall lock in

up and down positions.							____	____

Handle collars to have grease zerks and pull handles.			____	____

Loading doors shall be insulated with 3” closed-cell spray foam

polyurethane. 									____	____

Loading doors of tapered design with water lip to allow water shedding	____	____

7.0 Heating System

Shall be constructed with an air jacketed heating system			____	____

Air jacket shall be engineered to evenly transfer heat and prevent

scorching.									____	____

Hot air shall exhaust into the hopper, providing heat over the top of the

mix pile to assist in smooth even heating and provide a more

environmentally way to release the exhaust. Units with external

chimneys are deemed inefficient and are environmentally un friendly and

there for will not be accepted.							____	____

Shall use center heat riser to bring heat to center preventing asphalt

bridging.									____	____

Minimum burner capacity shall be minimum 105,000 BTU			____	____

Burner shall be diesel fueled							____	____

Diesel fuel tank shall be nestled inside frame rails for protection. Fuel

tanks located any where else will not be accepted.				____	____

Shall include a forced air burner system manufactured by Beckett Corp	____	____

Burner system shall feature electronic spark ignition and blower		____	____

Burner system shall offer flame-out shutdown				____	____

Burner to be mounted at the front of the unit, away from operator		____	____

7.0 Heating System (continued)						YES	NO

Burner shall be easily accessible and removable				____	____

Burner system operations shall be controlled at operator station		____	____

8.0 Discharge

Shovel platform shall be constructed of 1/4” 304 Stainless Steel to

prevent “burn outs”. Platforms constructed of plate steel will not be

accepted.									____	____

Hot box shall include minimum of two rear discharge doors 		____	____

Dual Discharge doors shall include gas assist opening system for easy

open/close.	 								____	____

Discharge doors shall not require latches or hooks to hold open		____	____

Design shall have sloped inner walls to move mix forward to allow easy

shovel.  									____	____

9.0 Controls

Controls shall be safely located at the rear of the unit closest to the

curb with clear polycarbonate cover to allow operator to see temperature

controls.									____	____

Control box shall feature:
     A) Automatic Temperature Controls 1/32 Din.				____	____

B) Burner On/Off Switch							____	____

C) Digital Electronic Temperature Gauge					____	____

D) Thermostat for hotbox							____	____
     F) Controls for OPTIONAL Strobe light or arrow stick controls 		____	____

10.0 Trailer

Trailer shall be municipal tandem axle					____	____

Shall have (2) cross members.

Trailer shall have electric brakes with break away kit			____	____

Hitch shall be 3” pintle style ring.						____	____

Trailer shall be fitted with height adjustable hitch minimum range

21” - 34”									____	____

Tandem Axles shall be a minimum 6000LB each.				____	____

10.0 Trailer (continued)							YES	NO

Shall have (2) one piece bolt-on shackles constructed of ¼” steel and

carry both axles. These allow proper wheel alignment and weight

distribution. Welded shackles will not be accepted.				____	____

Suspension shall be leaf spring type 						____	____

Shall have screw jack with minimum 5,000LB Capacity			____	____

Fenders shall be heavy duty miminum12 gauge steel bolt on design		____	____

Tires shall be 225/75R15 with steel welded wheel.				____	____

Minimum tire specifications shall be load range D tire.			____	____

Trailer electrical system shall be 12 volt DC battery with charging circuit.	____	____

All wire shall be run through the trailer frames for better protection.

Shall have NO exposed wiring. Anything else will be deemed

unacceptable.									____	____

Turn signals and stop lights shall be sealed beam grommeted.		____	____

Side markers shall be mounted at the rear and sides of the unit		____	____

Safety Chains shall be grade 40, attached eye bolts.				____	____

11.0 Available Options - Shall Include:					YES	NO

OPTION- Tack Tank:

Unit will be equipped with a heated tack tank with a minimum capacity

of 40 gallons with 3% expansion.  						____	____

Shall be rectangular in shape. Vertical tack tanks will not be accepted.	____	____

To have a 6"fill cap.  Diesel bottom fired configuration. Will have a 2"

molasses gate valve for draining the tank. 					 ____	____

Heated tack tank to be insulated with 2" of 1 1/2# hi-temperature

fiberglass insulation with 16 gauge outside cover. 				____	____

The thermostat shall have a digital readout that displays both set

and actual product temperature and be adjustable from 0-550ºF.		____	____

11.0 Available Options  (continued)					YES	NO

Optional Pumping System for Tack Tank:

To include a 12 hp, 2 Cylinder, liquid cooled, Kubota diesel engine with

electric start.									____	____

A 12 volt battery shall be included and located in a lockable battery box.

The engine shall power a hydraulic pump. 					____	____

The hydraulic pump shall power a hydraulic motor which will operate a

Viking HL-32 material pump.  Pump shall be capable of forward and

reverse positions.  								____	____

To include 15' of yellow ortec hose and 5' steel spray wand with an

on/off valve.  A 3-way valve shall be installed to allow for flushing of

pump and plumbing.								____	____

Compactor Plate Carrier:

Compactor Plate Carrier with hydraulic raise and lower for operator

convenience and shall have a spring lock and fold up out of the way

when not in use.								____	____

Electric Overnight Heat:

Shall have 110 Volt over night heaters. 2-750 watt 110 VAC heater to

heat and maintain material temperatures for cold mix materials

over night.									____	____

Shovel Cleaning Compartment:
Shall have a Shovel Cleaning Compartment constructed of 12 gauge

material with splash guard compartments, drain plug, and rain tight

cover. Shall hold (4) four shovels.						____	____

Tool Box:
12”x12”x24” Steel Tool Box.							____	____

Tool Holders:

(2) Stainless Steel Tool Holders-spring loaded clamps mounted

on each fender for holding rakes, shovels and lutes.				____	____

Arrow Stick:

Optional arrow stick for increased operator safety. Mounted on the top

rear of hopper with controller in the operators control panel.		____	____

Strobe Light:

Optional Flashing LED Light; Beacon or Flush mount.			____	____

11.0 Available Options (continued)						YES	NO

LP Hand Torch:

20# LP Bottle with hand torch and bottle rack.				____	____

Surge Type Brakes:

Surge type brakes in lieu of Electric Brakes.					____	____

Hose Reel:

Hose reel for tack hose and/or hand torch.					____	____

Lighting Options:

Standard 2 Light System:							____	____

2 Light LED System:								____	____

4 Light System:								____	____

4 Light LED System:								____	____

Diesel Burner Enclosure:

Lockable enclosure to protect burner from outside elements, also

vandal proof.									____	____

Spare Tire:

To include (1) 225/75R15 tire and mounting bracket.			____	____

Front Platform with Railing:

Shall be constructed of formed, stamped, grip strut material, to include

hand rail.									____	____

Wacker WP1550AW Plate Compactor:

19.5 x 23 plate  compactor with water tank for asphalt compaction.		____	____

Battery Charger:

To include (1) 12 volt type battery charger to maintain batteries in unit. 	____	____

12.0 Paint									
To be primed with primer. Frame to be painted highway black and

Hopper to be painted highway orange unless otherwise specified.

Paint to be a 2 part poly urethane paint minimum 6 mils thick.		____	____

13.0 Warranty

13.1 Manufacturer’s warranty shall be a minimum of 1 year.		____	____

14.0 Delivery

Equipment shall be furnished fully assembled, serviced and quality

checked for compliance with specification.					____	____

Two operator and parts manuals shall be furnished with the unit.		____	____

14.0 Delivery (continued):							YES	NO

Unit shall be delivered to DPW’ US facility as indicated			____	____

Acceptance shall be subject to inspection and approval of the DPW		____	____

Bidder shall state delivery time:

________________ Days (ARO) After Receipt of Order.

15.0 Prints

Engineering Prints shall be available upon request. Dealer shall provide

full package of Computer Aid Drawings (CAD) and 3D model of unit

with specified options to show DPW locations of options and standard

equipment. Hand Drafted prints will not be acceptable. 			____	____

Exceptions & Deviations

Bidder shall fully describe every variance exception and/or deviation.  List the item number here and fully explain any items in non-compliance with specification.   Additional sheets may be used if required.

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Price for (1) SPH 2.0 Pre-mix Heater or Equal

$_______________________ (FOB DESTINATION)

MAKE:______________________	MODEL:_____________________

Bidding Company _____________________________________________

Address______________________________________________________

City, State, Zip ________________________________________________

PH:_________________________FX:_______________________

Authorized Representative______________________________________

Signature_____________________________________________________

Date:_______________________

Email:_____________________________________