SPHOJ-3.0 Oil Jacketed Auger Delivery Patch Trailer

Bidding Specifications

1.0 INTENT

It is the intent of this specification to provide for the purchase of one (1) new and unused Oil Jacketed Auger delivery Patch Trailer to be used for the purpose of maintaining proper working temperature of hot mix asphalt.

The following specification is based upon a Stepp Mfg SPHOJ-3.0 Oil Jacketed Auger delivery Patch Trailer. The Public Works Department has evaluated different styles of asphalt hotbox equipment and has determined that this product is best suited for the DPW needs in terms of quality and features.  This specification shall not be interpreted as restrictive but rather as a measure of quality and performance against which all other Dump Style Premix Heaters will be compared.

In comparing proposals, comparison will not be confined to price only.  The successful bidder will be one whose product is judged as best serving the interests of the DPW when price, product, quality and delivery are considered. The DPW also reserves the right to reject any or all bids or any part thereof, and to waive any minor technicalities. A contract will be awarded to the bidder submitting the lowest responsible bid meeting the requirements.

2.0 EQUIVALENT PRODUCT

Bids will be accepted for consideration on any make or model that is equal or superior to the hot box specified.  Decisions of equivalency will be at the sole interpretation of the DPW.  A blanket statement that equipment proposed will meet all requirements will not be sufficient to establish equivalence. An original manufacture’s brochure of the proposed product is to be submitted with proposal.

3.0 INTERPRETATIONS

In order to be fair to all bidders, no oral interpretations will be given to any bidder, as to the meaning of the specification documents or any part thereof.  Every request for such a consideration shall be made in writing.  Based on such inquiry, the DPW may chose to issue an Addendum in accordance with local state laws.

4.0 GENERAL

The specification herein states the minimum requirements of the DPW. All bids must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The DPW will consider as irregular or non-responsive any and all bids that are not prepared and submitted in accordance with the bid document and specification, or any bid lacking sufficient technical literature to enable the DPW to make a reasonable determination of compliance to the specification.  It shall be the bidder’s responsibility to carefully examine each item of the specification. Failure to offer a completed bid or failure to respond to each section of the technical specification (COMPLY: YES NO) will cause the proposal to be rejected without review as non responsive. All variances, exceptions and/or deviations shall be fully described in the appropriate section. Deceit in responding to the specification will be cause for rejection.

5.0 SPECIFICATIONS

COMPLY

HOPPER:									YES	NO

Hopper shall have a capacity of 3 cubic yard. (4 ton)			____	____

The hopper shall have an overall dimension of 219” long

85” high and 89” wide.  							____	____

Hopper to be oil jacketed design with an 8” internal u shaped flue,

Submerged in the bottom of oil jacket. 					____	____

Flue shall have a 309L stainless steel liner					____	____

The oil jacket shall be constructed of 10 gauge steel and have an

external fill with a cold seal expansion tank.					____	____

The oil jacket shall have 2” of 1½# density high temperature

fiberglass insulation covered with a 16 gauge insulation jacket. 		____	____

Unit will be covered with two (2) 16 gauge steel insulated hoods,

insulated with poly urethane closed cell spray foam insulation. Opening

to form a funnel. Door to be sloped to shed water and shall be formed and

welded 2 piece construction. Channel frames are unacceptable.		____	____

Doors shall be equipped with 2 1 ½” hydraulic cylinders and be operated

with a hydraulic valve mounted on the rear of the unit.			____	____

Auger discharge will consist of a 74 1/8” long auger with 6” AR400

flighting. The flighting shall be 3/8” thick. The auger will have (2) sections

and (2) internal shafts. The auger shall sit in a AR400 auger troff  in the

bottom of the unit. Material will be dispensed on to a shoveling platform

that will fold up to discharge material on to road way for large patches.

Shovel platform shall be 10” off the ground.					____	____

Hopper will be in the Vee shape and have 32° walls to a straight vertical

Wall and have tapered tops to prevent asphalt build up.			____	____

Hopper shall have an internal oil filled baffle to prevent bridging of

material.							 		____	____

Oil jacket shall completely surround the sides not heads			____	____

COMPLY

ENGINE: 									YES	NO

The unit shall be powered by a 3 cylinder, liquid cooled, 26 HP,

Kubota diesel engine. The engine shall have a rain cover and have

a digital engine management system.  					____	____

Engine management system shall prevent engine failure if the engine

has low oil pressure, and over heat protection. Engine management

system shall also have a volt meter, hour meter, and glow plugs for

cold weather starting. 								____	____

Kubota engine shall be Tier 4 compliant D1105 26HP. 			____	____

HYDRAULIC SYSTEM:

The unit shall have a salami VDM8 Mono block hydraulic control valve

mounted on the rear center of the unit. The valve shall control the auger

in/out, top door open/close, optional tack pump forward/reverse, and

optional compactor plate carrier up/down. The valve shall also incorporate

a relief valve with a setting of 2500 Psi					____	____

The hydraulic pump shall be a Eaton Series 26 .84 CI with a 13.3 gpm

output and operate at 1500 PSI (3500 max).					____	____

The pump shall supply the top door cylinders, hydraulic motor for

the auger, motor for the optional tack pump and cylinder for the

optional compactor plate carrier. 						____	____

The auger motor shall be a 22.6 cu in displacement and have

350 lbs of torque.								____	____

TRAILER:

Shall be A-frame style constructed of 2”x 6”x 3/16” high strength

rectangular steel tubing reinforced at all stress points. 			____	____

All trailer wiring and fuel lines to be routed internally in the frame

where feasible and to exit the frame rail to the electric components.		____	____

The 3.0 cy trailer shall be equipped with 7000# leaf spring tandem

axle, unit shall have ST235/80/R16 load range E radial tires, heavy

duty replaceable 12 gauge steel fenders, pintle hitch, adjustable from

19” to 34” and adjustable screw jack.						____	____

The trailer shall have 2- one piece bolt on heavy duty shackle

constructed of ¼” steel.							____	____

COMPLY

YES	NO

The 7000# axles shall have an oil bath hub on each hub.			____	____

HEATING SYSTEM FOR HOPPER:

Unit shall include a 12 volt Beckett diesel burner.  Shall include

electronic spark ignition and blower and flame out protection. Burner

to be fired into an 8” flue with stainless steel liner.  				____	____

A thirty (30) gallon fuel tank shall be included.				____	____

Fuel tank shall be mounted in the front of the trailer on a bolt in cross-

member.									____	____

Burner exhaust gasses will be recycled and exhausted on the top of the

material to prevent bridging and capture the most efficiencies of the

burner system. The burner gases will then be exhausted through the top

covers of the units. 								____	____

Units using an external stack will be unacceptable due to the heat loss out

of the stack and not being environmentally friendly or efficient. 		____	____

Burner shall be rated at 105,000 BTU's. Burner system to have a

1/32nd Din electronic thermostat to control material and oil temperature.	____	____

Thermostat to have a LED digital read out displaying desired temperature

and actual temperature. The read out shall have a red and green LED

display.									____	____

The battery box shall contain 1 group 24 deep cycle battery

and be mounted on the front of the trailer frame.				____	____

LIGHTS:

Lights will be seal beam style. Rubber grommet mount. All lighting

shall meet state and federal regulations of the FMVSS. 			____	____

Unit will have 7 rear facing lights.						____	____

Stop, tail, turn and clearance lights will be mounted in the fenders.		____	____

Three light bar to be mounted on the top of the rear discharge door

assembly.									_____	____

COMPLY

PAINT									YES	NO

To be primed with primer and painted two tone. Frame, fenders, top doors,

fuel tank and discharge door to be painted black, hopper to be painted

highway orange, hi vis green, federal yellow, red, black or blue at no

additional charge. Other paint colors available upon request.  Paint to be a

2 part poly urethane paint minimum 6 mils thick.				____	____

WARRANTY:

One (1) year on workmanship and manufactured equipment.  		____	____

OPTIONAL EQUIPMENT

TACK TANK W/PUMPING SYSTEM:					YES	NO

Unit will be equipped with a heated tack tank with a capacity of 40

gallons.  									____	____

To have a 6"fill cap.  Diesel bottom fired configuration. Will have a 2"

molasses gate valve for draining the tank. 					 ____	____

Heated tack tank to be insulated with 2" of 1 1/2# hi-temperature

fiberglass insulation with 16 gauge outside cover. 				____	____

The thermostat shall have a digital LED readout that displays both set

and actual product temperature and be adjustable from 0-550ºF.		____	____

TACK TANK PUMPING SYSTEM 					YES 	NO

The hydraulic pump shall power a hydraulic motor which will operate a

Viking HL-32 material pump.  Pump shall be capable of forward and

reverse positions with hydraulic pressure relief built into valve.		____	____

To include 15' of yellow ortec hose and 5' steel spray wand with an

on/off valve.  A spring rewind hose reel shall be included. A 3-way

valve shall be installed to allow for flushing of pump and plumbing.	____	____

A WPC (wand pressure control) valve shall allow for recirculation or

spraying material.								____	____

OVERNIGHT HEATING SYSTEM 					YES 	NO

Shall have 220 Volt over night heaters. 2-1500 watt 220 VAC heater to

heat and maintain material temperatures for storage of hot mix materials

over night. To be submerged in oil jacket.					____	____

Shall have 110 volt overnight heaters. Shall have 2-750 watt heater to

maintain and heat cold patch materials. To be submerged in oil jacket.      	 ____	____

24 HOUR TIMER								YES 	NO

Shall include a 7 day programmable Timer for timed operation of burner.	____	____

SHOVEL CLEANING COMPARTMENT: 				YES 	NO

Shall have a Shovel Cleaning Compartment constructed of 12 gauge

material with splash guard compartments, drain plug, and rain tight

cover. Shall hold (4) four shovels. 						____	____

COMPACTOR PLATE CARRIER: 					YES 	NO

Compactor Plate Carrier with hydraulic raise and lower for operator

convenience and shall have a spring lock and fold up out of the way when

not in use.									____	____

PLATE COMPACTOR: 							YES 	NO

Plate compactor shall be a Wacker Model WP1550AW Plate

Compactor-  3300# with water tank.						____	____

Tool Box: 									YES 	NO
12”x12”x24” Steel Tool Box.							____	____

TOOL HOLDERS								YES 	NO

(2) Stainless Steel Tool Holders-spring loaded clamps mounted

on each fender for holding rakes, shovels and lutes.				____	____

ARROW STICK								YES	NO

Optional arrow stick for increased operator safety. Mounted on the top

rear of hopper with controller in the operators control panel.		____	____

STROBE LIGHT 								YES 	NO

Optional Flashing amber LED Light; Beacon or Flush mount.		____	____

LP HAND TORCH 								YES 	NO

20# LP Bottle with hand torch and bottle rack.				____	____

SURGE BRAKES 								YES 	NO

Surge type brakes in lieu of Electric Brakes.					____	____

HOSE REEL 								YES 	NO

Hose reel for tack hose and/or hand torch.					____	____

LIGHTING OPTIONS 							YES 	NO

2 Light LED light system. LED lights in lieu of incandescent lights.	____	____

4 Light System. Separate stop and running lights. For trucks with air

brakes and 7 round pin light connector.					____	____

4 Light LED System. Separate stop and running lights LED. For trucks

with air brakes	 and 7 round pin light connector.				____	____

Battery Charger:

Shall have a 12 volt marine type charger in a steel enclosure to maintain

battery on unit as needed. Charger shall have a weather tight, flush mounted

receptacle mounted on the rear of the box.					____	____

Exceptions & Deviations

Bidder shall fully describe every variance exception and/or deviation.  List the item number here and fully explain any items in non-compliance with specification.   Additional sheets may be used if required.

______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Price for (1) SPHOJ-3.0 Auger Style Pre-mix Heater	$_______________________

Price for Tack Tank w/Pumping System Option		$_______________________

TOTAL PRICE PER UNIT (option included)	$_______________________

DELIVERY DAYS (After Receipt of Order)		________________________

OPTIONAL FEATURES:							YES	NO