SPHD-3.0 Hot Pack Truck Mounted Hot Box

Bidding Specifications

1.0 INTENT

It is the intent of this specification to provide for the purchase of one (1) new and unused Slip in Style Asphalt Heater to be used for the purpose of maintaining proper working temperature of hot mix asphalt.

The following specification is based upon a Stepp Mfg SSPH-3.0 Hot Pack. The Public Works Department has evaluated different styles of asphalt hotbox equipment and has determined that this product is best suited for the DPW needs in terms of quality and features.  This specification shall not be interpreted as restrictive but rather as a measure of quality and performance against which all other Dump Style Premix Heaters will be compared.

In comparing proposals, comparison will not be confined to price only.  The successful bidder will be one whose product is judged as best serving the interests of the DPW when price, product, quality and delivery are considered. The DPW also reserves the right to reject any or all bids or any part thereof, and to waive any minor technicalities. A contract will be awarded to the bidder submitting the lowest responsible bid meeting the requirements.

2.0 EQUIVALENT PRODUCT

Bids will be accepted for consideration on any make or model that is equal or superior to the hot box specified.  Decisions of equivalency will be at the sole interpretation of the DPW.  A blanket statement that equipment proposed will meet all requirements will not be sufficient to establish equivalence. An original manufacture’s brochure of the proposed product is to be submitted with proposal.

3.0 INTERPRETATIONS

In order to be fair to all bidders, no oral interpretations will be given to any bidder, as to the meaning of the specification documents or any part thereof.  Every request for such a consideration shall be made in writing.  Based on such inquiry, the DPW may chose to issue an Addendum in accordance with local state laws.

4.0 GENERAL

The specification herein states the minimum requirements of the DPW. All bids must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The DPW will consider as irregular or non-responsive any and all bids that are not prepared and submitted in accordance with the bid document and specification, or any bid lacking sufficient technical literature to enable the DPW to make a reasonable determination of compliance to the specification.  It shall be the bidder’s responsibility to carefully examine each item of the specification. Failure to offer a completed bid or failure to respond to each section of the technical specification (COMPLY: YES NO) will cause the proposal to be rejected without review as non responsive. All variances, exceptions and/or deviations shall be fully described in the appropriate section. Deceit in responding to the specification will be cause for rejection.

5.0 SPECIFICATIONS

COMPLY

HOPPER:									YES	NO

Hopper shall have a capacity of 3 cubic yard. (4 ton)			____	____

The hopper shall have an overall dimension of 118” long

43” high and 73” wide.  Hopper to have a low profile design for

optimum visibility								____	____

Hopper floor shall be flat when the hoist is down to achieve the lowest

overall hopper height for driver visibility of operators at the rear of the

unit.										____	____

Hopper to be oil jacketed design with a 5” internal u shaped flue,

submerged in the bottom of oil jacket. 					____	____

Oil jacket shall heat the bottom and half way up the sides.			____	____

The oil jacket shall be constructed of 10 gauge steel and have an

internal fill with a cold seal expansion tank.					____	____

The oil jacket will have a 1” bottom drain and a 1” cold fill plug.		____	____

The oil jacket shall have 2” of 1½# density high temperature

fiberglass insulation covered with a 12 gauge insulation jacket. 		____	____

Unit will be covered with two (2) 16 gauge steel insulated hoods,

insulated with poly urethane closed cell spray foam insulation. Opening

to form a funnel.				 				____	____

Doors shall be equipped with a gas shock lift assist to reduce the weight

for the operator. Top door handles shall be spring swing handle lock in

the open and closed position							____	____

Discharge door shall be a single guillotine style door with gas shock assist.

Material will be dispensed on to a shoveling platform that will fold up

to discharge material on to road way for large patches.			____	____

Discharge door assembly shall be a bolt on for easy replacement if

damaged.									____	____

Discharge platform shall have a bolt on extender that shall fold up when

using the lower shovel platform.						____	____

Hopper shall have a heavy duty truck type, hydraulic scissor hoist, single 	COMPLY

cylinder for dumping material. Hoist to be mounted to a sub frame that is 	YES	NO

bolted to frame rails of the truck. Dual cylinder, non-sissor hoist shall not

be acceptable.									____	____

Hoist shall be powered by a 12Volt electric over hydraulic pump. 		____	____

Hoist to be mounted to a bolt on sub frame.					____	____

Hoist shall be rated to lift 12,000# and include a safety prop.		____	____

Power unit shall be located under the hopper attached to the bolt on

sub frame.									____	____

Unit shall be capable of dumping up to 52 degrees without the aid of

outriggers or drop legs. 							____	____

SHOVELING PLATFORM

The unit shall be equipped with a shoveling platform attached to the

Rear bumper of the subframe for the hoist.					____	____

HEATING SYSTEM FOR HOPPER:

Unit shall include a 12 volt Beckett diesel burner.  Shall include

electronic spark ignition and blower and flame out protection. Burner

to be fired into a 5” flue with stainless steel liner.  				____	____

A thirty (30) gallon fuel tank shall be included. 12 volt power must be

maintained from the tow vehicle at all times. 				____	____

Fuel tank shall be mounted in the front of the trailer on a bolt in cross-

member.									____	____

Burner exhaust gasses will be recycled and exhausted on the top of the

material to prevent bridging and capture the most efficiencies of the

burner system. The burner gases will then be exhausted through the top

covers of the units. 								____	____

Units using an external stack will be unacceptable due to the heat loss out

of the stack and not being environmentally friendly or efficient. 		____	____

Burner shall be rated at 105,000 BTU's. Burner system to have a

1/32nd Din electronic thermostat to control material and oil temperature.	____	____

COMPLY

Burner shall have a safety tilt switch to disable burner when unit is		YES	NO

raised. 										____	____

Thermostat to have a LED digital read out displaying desired temperature

and actual temperature. The read out shall have a red and green LED

display.									____	____

The battery box shall contain 1 deep cycle battery and the battery charger

and be mounted on the side of hopper	.				____	____

PAINT

To be primed with primer and painted two tone. Frame, fenders, top doors,

fuel tank and discharge door to be painted black, hopper to be painted

highway orange, hi vis green, federal yellow, red, black or blue at no

additional charge. Other paint colors available upon request.  Paint to be a

2 part poly urethane paint minimum 6 mils thick.				____	____

WARRANTY:

One (1) year on workmanship and manufactured equipment.  		____	____

Exceptions & Deviations

Bidder shall fully describe every variance exception and/or deviation.  List the item number here and fully explain any items in non-compliance with specification.   Additional sheets may be used if required.

______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Price for (1) SPHD 3.0 Dump Style Pre-mix Heater	$_______________________

DELIVERY DAYS (After Receipt of Order)		________________________

COMPLY

OPTIONAL FEATURES:							YES	NO

Battery Charger

Shall have a 12 volt marine type charger in a steel enclosure to maintain

battery on unit as needed. Charger shall have a weather tight, flush mounted

receptacle mounted on the rear of the box.					____	____

OVERNIGHT HEATING SYSTEM

Shall have 220 Volt over night heaters. 2-1500 watt 220 VAC heater to

heat and maintain material temperatures for storage of hot mix materials

over night.									____	____

Shall have 110 volt overnight heaters. Shall have 2-750 watt heater to

maintain and heat cold patch materials. To be submerged in oil jacket.       	 ____	____

24 HOUR TIMER

Shall include a 7 day programmable Timer for timed operation of burner.	____	____

TOOL BOX: 									
12”x12”x24” Steel Tool Box.							____	____

TOOL HOLDERS

(2) Stainless Steel Tool Holders-spring loaded clamps mounted

on each fender for holding rakes, shovels and lutes.				____	____

ARROW STICK

Optional arrow stick for increased operator safety. Mounted on the top

rear of hopper with controller in the operators control panel.		____	____

STROBE LIGHT

Optional Flashing amber LED Light; Beacon or Flush mount.		____	____

LP HAND TORCH

20# LP Bottle with hand torch and bottle rack.				____	____

WASH DOWN SYSTEM

Shall consist of 5 gallon tank, 12volt pump, hose and spray wand.	____	____

HOSE REEL

Hose reel for wash down hose and/or hand torch.				____	____

SHOVEL CLEANING COMPARTMENT:

Shall have a Shovel Cleaning Compartment constructed of 12 gauge

material with splash guard compartments, drain plug, and rain tight

cover. Shall hold (4) four shovels. 						____	____

COMPACTOR PLATE CARRIER:

Compactor Plate Carrier with electric raise and lower for operator

convenience and shall have a spring lock and fold up out of the way when

not in use.									____	____

WASH DOWN SYSTEM:

Wash down System with a 12V.D.C. pump with application hose and

wands for cleaning tools and hopper. Shall be pumped from truck fuel

tank and interfaced with burner shutoffs when the wash down is in

operation.			.						____	____

STAINLESS STEEL TOOL HOLDERS:

(2) Stainless Steel Tool Holders-spring loaded clamps mounted

on each fender for holding rakes, shovels and lutes.				____	____

ARROWSTICK:

Optional arrow stick for increased operator safety. Mounted on the top

rear of hopper with controller in the operators control panel.		____	____

STROBE LIGHTS:

Optional Flashing Beacon							____	____

HYDRAULIC DOOR OPERATION:

Shall have hydraulic operated doors to discharge material  and open top

doors.        									____	____

LP HAND TORCH:

20# LP Bottle with hand torch and bottle rack.				____	____

HOSE REEL:

Hose reel for tack hose, wash down and/or hand torch.			____	____

TOOL BOX:

12”x12”x24” Steel Tool Box.						____	____